## Slide 1: Smart Pill Companion
ROBOTICS RAY | IDEATION PROPOSAL
A low-cost robotic dispenser that reminds, verifies and alerts for elders who live alone
Falling Sun 2026 | 24-25 October
Notes: Open with the revealed Robotics theme and say in one sentence how the Smart Pill Companion fits it. Then state the hook: missed medicines cause preventable hospital visits.

## Slide 2: Problem & Abstract
SELECTION CRITERION 1 OF 5 | ABSTRACT & PROBLEM STATEMENT
Missed medicines cause preventable hospital visits.
ABSTRACT
Elders who live alone often miss or repeat doses. Smart Pill Companion is an Arduino-based robotic dispenser. It releases the right dose at the right time, confirms the pill was picked up, and alerts family if it was not. It also monitors storage, has a minor illness mode with saved prescriptions, and a PIN lock keeps settings safe.
Doses forgotten or doubled
Memory slips and complex schedules
No proof a dose was taken
Alarm clocks cannot verify
Family learns too late
No alert reaches caregivers
Notes: Problem in one line, then the three failure points: forgotten or doubled doses, no proof of intake, and family finding out too late. Add a cited statistic on medication non-adherence from WHO or a medical journal before presenting.

## Slide 3: Solution & Innovation
SELECTION CRITERION 2 OF 5 | PROPOSED SOLUTION & INNOVATION
01
Remind
LCD message plus gentle beeps
02
Dispense
Servo turns disc to the right slot
03
Verify
IR sensor sees pickup at the tray
04
Escalate
Alarm and lamp alert the family
WHAT MAKES IT DIFFERENT
Closed loop
Remind, verify, escalate
Works offline
Mega-based, no internet or app
Low cost
Target under ₹1,500 in parts
Notes: Walk the four steps left to right. The innovation is the closed loop: most pill reminders only ring, ours checks that the pill was picked up and escalates to family if not.

## Slide 4: Smart Features
SELECTION CRITERION 2 OF 5 | PROPOSED SOLUTION & INNOVATION
Storage Guardian
DHT11 shows temperature and humidity and warns if storage is unsafe
Touch + Knob Controls
4 touch buttons and a potentiometer set time, dose times and PIN digits
PIN Lock
Needed to change settings or clear alerts; 3 wrong tries lock it for 30 s
Minor Illness Mode
Pick an illness on the LCD, see the saved prescription, take the shown medicines from the opened box
Notes: Four features beyond the basic dispenser. A PIR sensor wakes the screen when someone waves a hand and shows the next dose time. The DHT11 shows temperature and humidity and warns when conditions are unsuitable for medicines. Four touch buttons and a potentiometer replace push buttons: the knob picks values, touch confirms. A PIN lock stops tampering with settings and alerts.

## Slide 5: System Design
SELECTION CRITERION 3 OF 5 | WORKING & SYSTEM DESIGN
INPUTS
CONTROLLER
OUTPUTS
IR tray sensor
DHT11 temp / humidity
4 touch buttons
Potentiometer knob
Software clock
Servos run from their own regulated 5 V supply with a common ground
Arduino Mega
State machine: IDLE, WAITING, ALERT
Servo pill disc
Servo: box lid
LCD: time, temp, humidity
RGB status light
Buzzer
Relay lamp or siren
Notes: Inputs on the left feed one Arduino Mega running a three-state program. Outputs on the right do the physical work: servo disc, LCD, LEDs, buzzer and a relay for a family alert lamp or siren.

## Slide 6: How It Works
SELECTION CRITERION 3 OF 5 | WORKING & SYSTEM DESIGN
IDLE
Green glow. Touch INFO to see next dose, temp, humidity
WAITING
Disc aligns slot, LCD says TAKE MEDICINE, blue light blinks, beeps
ALERT
Red flashing light and buzzer, relay lamp or siren, LCD shows FAMILY ALERT
dose time reached
no pickup in 10 min
Pill picked up: green light, “Well done!”, disc parks
Late pickup, or the caregiver touching ACK and entering the PIN, clears the alert
Notes: Three states. IDLE shows the clock. At dose time it moves to WAITING, where the disc aligns and the reminder starts. If the IR sensor sees the pill lifted, we celebrate and reset. If 10 minutes pass, ALERT escalates to the family lamp and siren.

## Slide 7: Minor Illness Mode
SELECTION CRITERION 2 OF 5 | PROPOSED SOLUTION & INNOVATION
01
Choose
Knob picks the illness, OK confirms
02
Prescription
LCD shows the saved prescription
03
Open
Servo lifts the medicine box lid
04
Close
OK closes the box, repeat use is locked
SAFETY BUILT IN
Saved prescriptions
Doctor-approved list per illness
Repeat lock
Same illness waits 4 hours
See a doctor
Shown if no relief in 2 days

## Slide 8: Status Light Colours
SELECTION CRITERION 3 OF 5 | WORKING & SYSTEM DESIGN
Green
All good
Standby: gentle pulse
Dose taken: solid green
Blue
Action needed
Time to take the dose: blinks
PIN, settings, illness menu: solid
Red
Problem
Missed dose: flashes with buzzer
Storage too hot or humid: solid
One 4-pin RGB LED, three colours, easy to read across the room.
Notes: The RGB LED uses only the three main colours. Green means all good, blue means the elder or caregiver needs to act, and red means a problem such as a missed dose or unsafe storage.

## Slide 9: Reliability & Testing
SELECTION CRITERION 4 OF 5 | RELIABILITY & TESTING
Test | Method | Pass criterion
Dispense accuracy | 50 cycles per slot; pill reaches tray | Every cycle succeeds
Pickup detection | Pills, fingertip, hand; bright, dim light | Detected every trial
Timeout and alert | Ignore a dose in demo and real time | Alert fires on schedule
Power stability | Servo moving with LCD, buzzer, relay on | No resets or glitches
DHT11 | DHT11 vs meter, 10 readings | Within ±2 °C, ±5 % RH
PIN lock | 3 wrong PINs, then the right PIN by knob | Locks 30 s, then accepts
Illness mode | Pick each illness; lid opens, list shown | Right medicines; lid closes; repeat blocked
Known limit: IR confirms pickup, not swallowing. Next step: weight sensor or camera.
Notes: These are planned tests with pass criteria we will log during the build. Be upfront about the known limit: the IR sensor proves the pill left the tray, not that it was swallowed.

## Slide 10: Applications & Future Scope
SELECTION CRITERION 5 OF 5 | REAL-LIFE APPLICATIONS & FUTURE SCOPE
Home care
Elders living alone
Care homes
Fewer manual rounds
Hospital wards
Night-time dosing
Rural clinics
Take-home doses
NOW
Mega prototype: 3 daily slots plus minor illness box
NEXT
RTC clock, battery backup, saved schedules
LATER
WiFi or GSM alerts, weight sensor, doctor-set illness lists, caregiver app